## Slide 1
Building Blocks
of
Local Area Networks

## Slide 2: Hubs
Hubs are essentially physical-layer repeaters:
  bits coming from one link go out all other links
  at the same rate
  no frame buffering
  no CSMA/CD at hub: adapters detect collisions
  provides net management functionality
twisted pair
hub

## Slide 3
Figure 15.1 Five categories of connecting devices

## Slide 4: Interconnecting with hubs
Backbone hub interconnects LAN segments
Extends max distance between nodes
But individual segment collision domains become one large collision domain
Can’t interconnect 10BaseT & 100BaseT
hub
hub
hub
hub

## Slide 5: Institutional network
hub
hub
hub
switch
to external
network
router
IP subnet
mail server
web server

## Slide 6: 10BaseT and 100BaseT
10/100 Mbps rate; latter called “fast ethernet”
T stands for Twisted Pair
Nodes connect to a hub: “star topology”; 100 m max distance between nodes and hub
twisted pair
hub