## Slide 1: Spanning Tree Protocol (IEEE 802.1d)

## Slide 2
Note :
This presentation refers to Bridges ;
  But same is applicable to Switches.
[ ‘then’ bridges are ‘today’ Switches ]

## Slide 3: Danger of Loops
Consider the two LANs that are connected by two bridges.
Assume host n is transmitting a frame F with unknown destination.
What is happening?
Bridges A and B flood the frame to LAN 2.
Bridge B sees F on LAN 2 (with unknown destination), and copies the frame back to LAN 1
Bridge A does the same.
The copying continues
Where’s the problem? What’s the solution ?
F
F
F
F
F
F
F

## Slide 4: Spanning Tree Protocol (IEEE 802.1d)
The Spanning Tree Protocol (SPT) is a solution to prevent loops when forwarding frames between LANs
The SPT is standardized as the IEEE 802.1d protocol
The SPT organizes bridges and LANs as spanning tree in a dynamic environment
  Frames are forwarded only along the branches of the spanning tree
  Note: Trees don’t have loops
Bridges that run the SPT are called transparent bridges
Bridges exchange messages to configure the bridge (Configuration Bridge Protocol Data Unit or BPDUs) to build the tree.

## Slide 5: Configuration BPDUs

## Slide 6: What do the BPDUs do?
With the help of the BPDUs, bridges can:
Elect a single bridge as the root bridge.
Calculate the distance of the shortest path to the root bridge
Each LAN can determine a designated bridge, which is the bridge closest to the root. The designated bridge will forward packets towards the root bridge.
Each bridge can determine a root port, the port that gives the best path to the root.
Select ports to be included in the spanning tree.

## Slide 7: Concepts
Each bridge as a unique identifier: Bridge ID Bridge ID = Priority : 2 bytes Bridge MAC address: 6 bytes
      Priority is configured
      Bridge MAC address is lowest MAC addresses of all ports
Each port of a bridge has a unique identifier (port ID).
Root Bridge: The bridge with the lowest identifier is the root of the spanning tree.
Root Port: Each bridge has a root port which identifies the next hop from a bridge to the root.

## Slide 8: Concepts
Root Path Cost: For each bridge, the cost of the min-cost path to the root.
Designated Bridge, Designated Port: Single bridge on a LAN that provides the minimal cost path to the root for this LAN: - if two bridges have the same cost, select the one with highest priority - if the min-cost bridge has two or more ports on the LAN, select the port with the lowest identifier
Note: We assume that “cost” of a path is the number of “hops”.

## Slide 9: Steps of Spanning Tree Algorithm
Each bridge is sending out BPDUs that contain the following information:
The transmission of BPDUs results in the distributed computation of a spanning tree
The convergence of the algorithm is very quick
root bridge (what the sender thinks it is) root path cost for sending bridge Identifies sending bridge Identifies the sending port
root ID
cost
bridge ID
port ID

## Slide 10: Selecting the Ports for the Spanning Tree
Each bridges makes a local decision which of its ports are part of the spanning tree
Now B can decide which ports are in the spanning tree:
    B’s root port is part of the spanning tree
    All designated ports are part of the spanning tree
    All other ports are not part of the spanning tree
B’s ports that are in the spanning tree will forward packets (=forwarding state)
B’s ports that are not in the spanning tree will not forward packets (=blocking state)

## Slide 11: Building the Spanning Tree
Consider the network on the right.
Assume that the bridges have calculated the designated ports (D) and the root ports (P) as indicated.
What is the spanning tree?
  On each LAN, connect R ports to the D ports on this LAN

## Slide 12: Example
Assume that all bridges send out their BPDU’s once per second, and assume that all bridges send their BPDUs at the same time
Assume that all bridges are turned on simultaneously at time T=0 sec.

## Slide 13: Example: BPDU’s sent by the bridges
 | Bridge 1 | Bridge 2 | Bridge 3 | Bridge 5 | Bridge 6 | Bridge 7
T=0sec | (1,0,1,port) sent on ports: A,B | (2,0,2,port) ports A,B | (3,0,3,port) ports A,B,C | (5,0,5,port) ports A,B,C | (6,0,6,port) ports A,B,C,D | (7,0,7,port) ports A,B,C
T=1sec | (1,0,1,port) A,B | (2,0,2,port) A,B | (1,1,3,port)A,C | (1,1,5,port) B,C | (1,1,6,port) A,C,D | (1,1,7,port) A
T=2sec | (1,0,1,port) A,B | (1,2,2,port) none | (1,1,3,port) A,C | (1,1,5,port) B,C | (1,1,6,port) D | (1,1,7,port) none
In the table (1,0,1,port) means that the BPDU is (1,0,1,A) if the BPDU is sent on port A and (1,0,1,B) if it is sent on port B.
At T=1, Bridge 7 receives two BPDUs from Bridge 1: (1,0,1,A) and (1,0,1,B). We assume that A is numerically smaller than B. If this is not true, then the root port of Bridge 7 changes.

## Slide 14: Example: Settings after convergence
 | Bridge 1 | Bridge 2 | Bridge 3 | Bridge 5 | Bridge 6 | Bridge 7
Root Port | - | A | B | A | B | B
Designated Ports | A,B | - | A,C | B,C | D | -
Blocked ports | - | B | - | - | A,C | A,C
Resulting tree: