## Slide 1: VLANs: motivation
consider:
CS user moves office to EE, but wants connect to CS switch?
single broadcast domain:
  all layer-2 broadcast traffic (ARP, DHCP, unknown location of destination MAC address) must cross entire LAN
  security/privacy, efficiency issues
Computer
Science
Electrical
Engineering
Computer
Engineering

## Slide 2: VLANs
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches

## Slide 3: Port-based VLAN
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
router
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 4: VLANS spanning multiple switches
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1

## Slide 5
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (12 bit VLAN ID field,
3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q VLAN frame format
802.1 frame
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type

## Slide 6
15-3 VIRTUAL LANs
We can roughly define a virtual local area network (VLAN) as a local area network configured by software, not by physical wiring.

## Slide 7
Figure 15.15 A switch connecting three LANs

## Slide 8
Figure 15.16 A switch using VLAN software

## Slide 9
Figure 15.17 Two switches in a backbone using VLAN software

## Slide 10
VLANs create broadcast domains.
Note