## Slide 1: Synthesis: a day in the life of a web request
journey down protocol stack complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 2: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 3: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 4: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 5: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 6: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demux’ed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 7: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)

## Slide 8: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed